## Slide 1: Application: Tank Sloshing – Model Description
Fluids and tank system starts at rest (equilibrates for 1 ms). Tank then accelerates to 20 m/s, then decelerates to 0m/s to create sloshing.
An impactor moving at -50 m/s strikes the tank.
Unit system: kg-mm-ms-K; Total run time = 40 ms.
-50 m/s
20 m/s
S1 = Lagr. shell tank
S5 = rigid bracket ...

## Slide 2: Application: Tank Sloshing – Simulation
S-ALE: 1h41m; ALE: 2h30m (32% speedup)
MPP dev.105342 single precision 12 CPU

## Slide 3: Application: Tank Sloshing – Model Setup 1
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
1 | 202 | 2000001 | 2000001 |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
1001 | 1002 | 1003 | 34081 | 234 | 
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1001 |  |  | 363.31729
1 |  | -500. | 
75 |  | 525. | 
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1002 |  |  | -107.0625
1 |  | -375. | 
57 |  | 375. | 
*ALE_STRUCTURED_MESH_CONTROL_POINTS |  |  | 
1003 |  |  | 
1 |  | -90. | 
23 |  | 260. | 
MSHID: Mesh ID ( for future use)
PID: Part ID assigned to the mesh
NO NEED to define *PART card
NBID: Starting Node ID
EBID: Starting Element ID
NID0: Origin Node ID
LCSID: Local Coordinate System ID

## Slide 4: Application: Tank Sloshing – Model Setup 1
*ALE_STRUCTURED_MESH |  |  |  |  | 
MSHID | PID | NBID | EBID |  | 
1 | 202 | 2000001 | 2000001 |  | 
CPIDX | CPIDY | CPIDZ | NID0 | LCSID | 
1001 | 1002 | 1003 | 34081 | 234 | 
*NODE |  |  | 
34081 | -3.6331729e+2 | -1.070625e+2 | 0.0000000
33961 | -3.432692e+2 | -1.070625e+2 | 0.0000000
25032 | -3.6331729e+2 | 2.0965269e+2 | 0.0000000
*DEFINE_COORDINATE_NODES |  |  |  | 
234 | 34081 | 33961 | 25032 | 1
Node 34081, 33961, 25032 are three nodes on the Lagrange rigid body part

## Slide 5: Application: Tank Sloshing – Model Setup 2
*ALE_MULTI-MATERIAL_GROUP | 
PID | PTYPE
2 | 1
3 | 1
4 | 1
*PART |  |  |  | 
PID | SECID | MID | EOSID | HGID
2 | 2 | 2 | 2 | 2
3 | 3 | 3 | 3 | 3
4 | 4 | 4 | 4 | 4
1 to 1
*SECTION should always be 11. Same SECID OK.
*HOURGLASS form and coefficient should always be 1 and 1.0e-6. Same HGID OK.
PIDs not used elsewhere. Only to be put into *ALE_MULTI-MATERIAL_GROUP card.
PID | MATERIAL | AMMG
2 | AIR outside | 1
3 | Vapor inside | 2
4 | Fuel inside | 3

## Slide 6: Application: Tank Sloshing – Model Setup 3
*INITIAL_VOLUME_FRACTION_GEOMETRY |  |  |  |  |  |  | 
SID | IDTYP | BAMMG |  |  |  |  | 
202 | 1 | 3 |  |  |  |  | 
TYPE | FILLOPT | FAMMG |  |  |  | “3 = PLANE” | 
3 | 0 | 2 |  |  |  |  | 
X0 | Y0 | Z0 | X1 | Y1 | Z1 |  | 
-6.5 | -300.0 | 132.0 | 0.0 | 0.0 | 0.0 |  | 
TYPE | FILLOPT | FAMMG |  |  |  | “1 = PART/PSET” | 
1 | 1 | 1 |  |  |  |  | 
SETID | SETTYP | NORMD |  |  |  |  | 
15 | 0 |  |  |  |  |  | 
1. All to “Fuel”; 2. Above the plane to “Vapor”; 3. Outside the part 1+5 to “Air”

## Slide 7: Application: Explosion – Model Setup FSI
*CONSTRAINED_LAGRANGE_IN_SOLID |  |  |  |  |  |  | 
SLAVE | MASTER | SSTYP | MSTYP | NQUAD | CTYPE | DIREC | MCOUP
15 | 202 | 0 | 1 | 2 | 4 | 2 | -11
START | END | PFAC | FRIC | FRCMIN | NORM | NORMT | DAMP
 |  | -3 |  |  | 1 |  | 
CQ | HMIN | HMAX | ILEAK | PLEAK |  |  | 
 |  |  | 2 | 0.1 |  |  | 
Couple tank to air outside
Couple tank to vapor inside
*CONSTRAINED_LAGRANGE_IN_SOLID |  |  |  |  |  |  | 
SLAVE | MASTER | SSTYP | MSTYP | NQUAD | CTYPE | DIREC | MCOUP
15 | 202 | 0 | 1 | 2 | 4 | 2 | -22
START | END | PFAC | FRIC | FRCMIN | NORM | NORMT | DAMP
 |  | -3 |  |  |  |  | 
CQ | HMIN | HMAX | ILEAK | PLEAK |  |  | 
 |  |  | 2 | 0.1 |  |  | 

## Slide 8: Application: Explosion – Model Setup FSI
*CONSTRAINED_LAGRANGE_IN_SOLID |  |  |  |  |  |  | 
SLAVE | MASTER | SSTYP | MSTYP | NQUAD | CTYPE | DIREC | MCOUP
15 | 202 | 0 | 1 | 2 | 4 | 2 | -33
START | END | PFAC | FRIC | FRCMIN | NORM | NORMT | DAMP
 |  | -4 |  |  |  |  | 
CQ | HMIN | HMAX | ILEAK | PLEAK |  |  | 
 |  |  | 2 | 0.1 |  |  | 
Couple tank to Fuel inside
Different combinations of coupling cards can be defined.
1 card only
  tank to inside vapor + fuel
2 cards
  tank to inside vapor + fuel
  tank to outside air
3 cards
  tank to inside vapor
  tank to inside fuel
  tank to outside air

## Slide 9: Application: Explosion – Model Setup MISC
*CONTROL_ALE |  |  |  |  |  |  | 
DCT | NADV | METHOD | AFAC | BFAC | CFAC | DFAC | EFAC
 | 1 | 1 |  |  |  |  | 
START | END | AAFAC | VFACT | PRIT | EBC | PREF | NSIDEBC
 |  |  |  |  |  | 1.01325e-4 | 
Include hydrostatic pressure in the calculation
*INITIAL_HYDROSTATIC_ALE |  |  |  | 
SID | STYPE | VECID | GRAV | PBASE
202 | 1 | 1 | 9.81e-3 | 1.01325e-4
NID | MMGBelow |  |  | 
294095 | 1 |  |  | 
900001 | 2 |  |  | 
900002 | 3 |  |  | 
*LOAD_BODY_Z | 
LCID | SF
6 | 0.00981